## Slide 1
NNMixer on ArduPilot
How MAVProxy, ArduRover, the PPO network and MuJoCo are connected
Roberto Navoni — DelphyAI LAB · r.navoni74@gmail.com · 24 September 2026
Repo: github.com/virtualrobotix/microduck-ap-ppo-sitl · fork ArduPilot: virtualrobotix/ardupilot @ microduck-ppo
One ArduRover firmware. The neural network (61 observations → 14 servos, 50 Hz) is a scheduler task. MuJoCo is the robot body, attached to the SITL like an external physics engine. Commands come from MAVProxy over MAVLink.
Developed by Roberto Navoni : r.navoni74@gmail.com

## Slide 2
1. Three processes, two links
In simulation: GCS, firmware, robot body. On hardware the third process is the real robot.
Developed by Roberto Navoni : r.navoni74@gmail.com
2
MAVProxy (GCS)
operator or script
arm / disarm
stick: rc N <pwm>
mode manual / hold
param set NNM_*
PPO_* telemetry
ArduRover SITL
(a single ardurover binary)
RC_Channels → twist in SI units
AP_InertialSensor → gyro, gravity
AP_NNMixer: PPO network 50 Hz
SRV_Channels: 14 PWM
SIM_JSON backend
MuJoCo plant
plant/mujoco_json_plant.py
14 XL330 servos (BAM model)
physics 200 Hz (5 ms)
IMU, joint encoders
viewer / video
MAVLink tcp:5760
STATUSTEXT, NAMED_VALUE_FLOAT
udp:9002 16 PWM
udp:9003 JSON
Lock-step: the SITL sends the PWM and waits for the JSON; MuJoCo takes one 5 ms step per frame (SIM_RATE_HZ 200). The PPO task runs every 4 frames = 50 Hz, as in training.
The PPO task has no link to MuJoCo: it only sees ArduPilot APIs. Replacing the plant with a real IMU + Dynamixel bus does not change a line of AP_NNMixer.

## Slide 3
2. Inside ArduRover: the 50 Hz loop of AP_NNMixer
Everything the network sees goes through ArduPilot's standard libraries.
Developed by Roberto Navoni : r.navoni74@gmail.com
3
ArduRover — scheduler (SCHED_LOOP_RATE 200)
AP_InertialSensor
gyro, accel FRD
Joint feedback
q, q̇ (14) from sitl->state
RC_Channels
sticks 1/2/4 → vx vy ωz
History
previous action (14)
Gravity filter
IMU-only, no EKF
build_obs
61 float32
trunk FLU frame
Forward C
mean/std + network
MLP
≈0.37 ms
SRV_Channels
Scripting1..14 → PWM
q_target = q0 + a
applied a → history (obs[34:48]) at the next tick
• update_attitude() at loop rate: propagates the gravity direction with the gyro, corrects it with the accelerometer (NNM_ATT_TAU 0.5 s)
• update() at 50 Hz: obs → forward → clip → PWM
• Failsafe: disarmed, joint feedback missing or older than NNM_WD_MS → action 0 = stand pose (also in the history)
• HOLD (NNM_HOLD_MODE 4) → twist 0
• PWM: 1500 + q/0.003 (1 µs = 3 mrad), SERVOn 800..2200

## Slide 4
3. Sensor path: from MuJoCo to the observation
Different frames, different units: the plant speaks ArduPilot (FRD/NED), the task speaks training (FLU).
Developed by Roberto Navoni : r.navoni74@gmail.com
4
MuJoCo
gyro/accel at the IMU site (FLU)
trunk quaternion (z-up)
qpos, qvel of 14 joints
JSON udp:9003
imu.gyro, imu.accel_body (FRD)
quaternion (NED→FRD)
joints.jpos / jvel
SITL / SIM_JSON.cpp
→ simulated INS (gyro, accel)
→ sitl->state.joint_pos/vel
(extension added by this repo)
AP_NNMixer
gyro FRD→FLU: (x, −y, −z)
gravity: filter → (x, −y, −z)
q − q0, q̇
Frame conversion (done by the plant)
• vectors: (x, y, z)_MuJoCo → (x, −y, −z)_ArduPilot — gyro, accel, position, velocity
• quaternion: (w, x, y, z) → (w, x, −y, −z)
• standing: accel_body = (0, 0, −9.81) as ArduPilot expects; projected gravity in the task = (0, 0, −1) as in training
Lesson from the first test
• ArduRover defaults to INS_GYRO_FILTER 4 Hz: the gyro reached the network tens of ms late → fall within 1 s
• INS_GYRO_FILTER 0 (or 40) → stable. No slow low-pass on the gyro that feeds the policy, on hardware too

## Slide 5
4. Command path: from MAVProxy to the twist
Every command typed in MAVProxy is a standard MAVLink message; ArduPilot was not modified here.
Developed by Roberto Navoni : r.navoni74@gmail.com
5
MAVProxy command | MAVLink message | What ArduRover does | Effect on the network
arm throttle [force] | COMMAND_LONG MAV_CMD_COMPONENT_ARM_DISARM p1=1 | AP_Arming → soft armed | PPO_FAIL 1→0, servos live, the policy keeps it standing
rc 2 2000 | RC_CHANNELS_OVERRIDE chan2=2000 (from sysid 255) | RC_Channels: norm_input_dz = +1.0 | obs[48] vx = +1.0 × NNM_VX_MAX = 0.4 m/s
rc 1 1800 | RC_CHANNELS_OVERRIDE chan1=1800 | norm = +0.6 | obs[49] vy = 0.6 × 0.3 = 0.18 m/s
rc 4 2000 | RC_CHANNELS_OVERRIDE chan4=2000 | norm = +1.0 | obs[50] ωz = 1.0 rad/s
mode hold | COMMAND_LONG MAV_CMD_DO_SET_MODE custom_mode=4 | Rover in HOLD | NNM_HOLD_MODE → twist forced to 0: stands still
param set NNM_POLICY 0 | PARAM_SET | AP_Param | next tick uses the MLP network
disarm | COMMAND_LONG ARM_DISARM p1=0 | soft disarmed | action 0, history cleared, PWM 0 (plant: idle)
Return telemetry (NAMED_VALUE_FLOAT every 0.5 s): PPO_MS forward time, PPO_PGZ gravity z (standing ≈ −1), PPO_VX command, PPO_FAIL state.
DataFlash log NNM / NNMQ / NNMV / NNMA: every tick with the 61 observations and 14 actions → tools/log_parity.py replays them through the ONNX (parity 2.5e-7).

## Slide 6
5. Actuator path: from the action to the servos
The network outputs offsets in radians; ArduPilot carries them as PWM; the plant converts them back to position targets.
Developed by Roberto Navoni : r.navoni74@gmail.com
6
Network
a[14] rad
clip ±NNM_ACT_MAX
q_target
= q0 + a
q0 = STAND2 pose
SRV_Channels
pwm = 1500 + q/0.003
functions 94..107 (Scripting1..14)
Plant / robot
SITL: servo packet udp:9002 → MuJoCo BAM
HW: Dynamixel bus (ticks)
• Why Scripting1..14: existing servo functions ArduPilot never touches (no mixer, no ESC), writable with SRV_Channels::set_output_pwm without modifying SRV_Channel
• Resolution 3 mrad/µs: enough for the XL330 (1.5 mrad/tick); on hardware Robotis ticks are used and the conversion disappears
• PWM 0 = 'not driving' (disarmed): the plant keeps the duck pinned upright; on hardware this is torque off
• The action sent to the servos is the one stored in the history: at the next step the network sees what was actually applied
• Feedback: the plant returns the real joint q and q̇; the task never uses the targets as a surrogate

## Slide 7
6. The ArduRover integration, file by file
Fork virtualrobotix/ardupilot, branch microduck-ppo, on upstream master of 24 Sep 2026. 7 files touched + 1 new library.
Developed by Roberto Navoni : r.navoni74@gmail.com
7
File | Change | Why
libraries/AP_NNMixer/ (new) | AP_NNMixer.{h,cpp}, nnmixer_infer.{h,c}, policy_mlp.h, AP_NNMixer_config.h | the task: obs, gravity filter, history, sticks, servos, NNM_*, log, telemetry; network in C
Rover/Parameters.h / .cpp | member g2.nnmixer; AP_SUBGROUPINFO "NNM_" index 63 | NNM_* parameters visible from the GCS and stored in EEPROM
Rover/Rover.cpp | SCHED_TASK_CLASS update_attitude 400 Hz (→ loop rate), update 50 Hz | the task enters the scheduler like any other library
Rover/wscript | + 'AP_NNMixer' | links the library into the ardurover binary
libraries/SITL/SIM_JSON.h / .cpp | type DATA_FLOAT_ARRAY14; keys joints/jpos, joints/jvel; copied into sitl->state | the physics backend delivers the joints the same way it delivers the IMU
libraries/SITL/SITL.h | sitl_fdm: joint_pos[16], joint_vel[16], joint_count, joint_time_us | SITL source of the joint feedback; on HW a Dynamixel driver replaces it
No change to RC_Channels, SRV_Channel, AP_InertialSensor, AP_Arming, GCS_MAVLink: the task uses their public APIs. AP_NNMIXER_ENABLED is 1 on SITL; boards must opt in (weights ~770 KB of flash as float32).
SITL parameters (sitl/nnmixer.parm): SERVO1..14_FUNCTION 94..107, SERVOn_MIN/MAX 800/2200, SIM_RATE_HZ 200, SCHED_LOOP_RATE 200, INS_GYRO_FILTER 0, ARMING_CHECK 0, NNM_ENABLE 1.

## Slide 8
7. Timing and synchronisation
A single timeline, driven by the JSON lock-step.
Developed by Roberto Navoni : r.navoni74@gmail.com
8
MuJoCo (5 ms)
SITL frame / INS (5 ms)
ArduRover loop (5 ms)
AP_NNMixer::update (20 ms)
MAVProxy (asynchronous)
200 ms
• The SITL sends the PWM → MuJoCo takes 1 step (5 ms) → replies with the JSON → the SITL advances its clock by 5 ms. Neither side can run ahead.
• The 50 Hz task sees 4 physics steps per action, as in training (decimation 4). The forward pass takes ~0.37 ms on the Mac; 1–2 ms estimated on an STM32H7.

## Slide 9
8. From .pt to C: how the trained network enters the firmware
The observation normalizer is part of the network, not of the simulator.
Developed by Roberto Navoni : r.navoni74@gmail.com
9
model_1999.pt
PyTorch: actor, critic,
optimizer, normalizer
(mjlab + rsl_rl, 2048×2000)
.onnx
actor(normalizer(obs))
Sub(mean) → Div(std) →
Gemm/ELU
policy_mlp.h
static const float
mean[61], std[61], weights, q0
773 KB MLP
nnmixer_infer.c
forward float32
expf, no heap
identical SITL / MCU
AP_NNMixer
update()
50 Hz
scripts/export.py
tools/export_policy_c.py
#include
Verified at three points
• tools/parity_check.py: 2201 observations → ONNX Runtime vs the C binary: max 3.8e-6 (MLP)
• tools/log_parity.py: observations logged by the firmware while running → ONNX vs the actions the firmware sent: max 2.5e-7
• tools/policy_rollout_plant.py: the same policy on the same plant without ArduPilot — separates plant issues from firmware issues
The network (NNM_POLICY)
• 0 = MLP 61→512→256→128→14 ELU, 197 896 parameters, 0.37 ms

## Slide 10
9. What changes on hardware
Only the third process: the MuJoCo plant becomes the robot. AP_NNMixer does not change.
Developed by Roberto Navoni : r.navoni74@gmail.com
10
Block | In SITL (today) | On the robot
IMU | MuJoCo → JSON → simulated INS | flight-controller IMU (same AP_InertialSensor)
Joint feedback | JSON joints → sitl->state | Dynamixel bus driver (present position/velocity) → set_joint_feedback()
Servo outputs | SRV_Channels → JSON PWM packet → MuJoCo BAM | SRV_Channels → Robotis protocol (ticks) on the XL330
Commands | MAVProxy rc / mode / arm | real RC + GCS, identical
Network | policy_mlp.h in C, 0.37 ms on the Mac | same source; STM32H7: 1–2 ms estimated (MLP)
IMU filters | INS_GYRO_FILTER 0 | same rule: no slow LPF on the gyro that feeds the policy
The real constraint is the microcontroller budget: ~2×10⁵ MAC per step (MLP) at 50 Hz on top of EKF, buses and logging. Next step: the same update() compiled on a Nucleo H7, 1000 forward passes, p50/p99 measured.

## Slide 11
10. The demo and the results
scripts/demo_mavproxy.py: one command starts plant, SITL and MAVProxy and types the operator's sequence.
Developed by Roberto Navoni : r.navoni74@gmail.com
11
Sequence typed into MAVProxy
• param set NNM_POLICY 0 · param set NNM_ENABLE 1
• mode manual · rc all 1500 · arm throttle → 6 s standing
• rc 2 2000 → forward 3 s · rc 2 1000 → backward 2 s
• rc 1 1800 → lateral 2 s · rc 4 2000 → 90° turn (integral of ATTITUDE.yawspeed) · rc 2 2000 → forward 5 s
• mode hold → twist 0 · mode manual · disarm
In the video (docs/media/demo_mavproxy_mlp.mp4)
• credit box and panel on the left: MAVProxy command and the matching MAVLink message
• badge on the right: phase and commanded twist in SI units
• barra in basso: tempo, posizione, tilt del robot in MuJoCo
 | MLP
Parity C vs ONNX | 3.8e-6
In-situ parity (firmware log) | 2.5e-7
Forward pass in SITL | 0.37 ms
Weights in flash (float32) | 773 KB
HIL battery, 8 steps | 8/8 PASS
Forward 0.3/0.4 m/s, 15 s | no fall
Speed tracking (~0.2 m/s at a 0.4 command) is the same as the Python rollout on the same CPU plant: it is the MuJoCo-CPU vs MuJoCo-Warp gap of training, not the ArduPilot integration.